 OPEN SAS photos for OCAD

SASPlanet can download photos from multiple sources and merge them. Problem is getting them georeferenced to use British National Grid. Also lack of documentation. By using GeoTIFF output it is possible to do this by hand. Need to specify location of top left of image, and meters/pixel of the file produced.

Recipe

1) Identify two points NW and SE of the area to be mapped with a well defined Grid reference.

2) In SASPlanet create record lat and long of these points.

3) Create a rectangular selection with these points in Selection Manager

4) Download images with zoom level 19

5) Reopen manager and choose stitch

 Choose Geotiff output format
Define a place to save file
Set zoom level to 19
Choose Projection Mercator / WGS84 / EPSG 3395
Choose ouput .w georeferencing file

Note size of output in pixels (can also find it fromfile properties in Explorer )

6) Open the generated .tifw file and change the last two numbers to match the grid reference of top left point.

Divide difference in eastings of two corners by number of pixels in x direction

to obtain pixel size in the x-direction in map units/pixel

Enter this in the first row
Repeat for the y direction and enter in fourth row ( -ve value in 4th row)

7) Open Map in OCAD, ensure it is rotated to grid north

8) Open map as background map, compare to other source (OS) to fine tune.

This is almost but not quite right.

Parameter Name	Parameter Value or Parameter File	Unit of Measure	Sign Reversible
Latitude of natural origin		degree	No
Longitude of natural origin		degree	No
Scale factor at natural origin	0.9996012717	unity	No
False easting	400000	metre	No
False northing	-100000	metre	No

We need British National Grid epsg number 19916

We get 3395

Parameter Name	Parameter Value or Parameter File	Unit of Measure	Sign Reversible
Latitude of natural origin		degree	No
Longitude of natural origin		degree	No
Scale factor at natural origin	1	unity	No
False easting	0	metre	No
False northing	0	metre	No

The aerial photo will taper slightly more than it should so the bottom is wider than the top. This can be fine tuned by doing “Adjust background map”. Use one point at top, and two at edges of bottom to achieve perfect fit.

We can use the program gdalwarp.exe to convert the tiff file. These are the steps

Output from SASPlanet in format WGS 84. We need to first convert to OSGB 36, and then convert
to British National Grid ( see: https://communityhub.esriuk.com/geoxchange/2012/3/26/coordinate-systems-and-projections-for-beginners.html)

The commands are:

Convert between Geographic Coordinate systems
 gdalwarp.exe -t_srs 'EPSG:4277' .\SASPlanetAerialPhotosEPSG3395.tif .\SASPlanetAerialPhotosEPSG4277.tif

Project to National Grid
> gdalwarp.exe -t_srs $env:GDAL_DATA\OSGB1936ToBritishNationalGrid.prj SASPlanetAerialPhotosEPSG4277.tif SASPlanetAerialPhotosBNG.tif

The numbers are epsg numbers (see here: https://www.epsg-registry.org/)

The file OSGB1936ToBritishNationalGrid.prj.txt contains:
PROJCS["OSGB 1936 / British National Grid",
    GEOGCS["OSGB 1936",
        DATUM["OSGB_1936",
        SPHEROID["Airy 1830",6377563.396,299.3249646,
        AUTHORITY["EPSG","7001"]],
        TOWGS84[446.448,-125.157,542.06,0.15,0.247,0.842,-20.489],
        AUTHORITY["EPSG","6277"]],
        PRIMEM["Greenwich",0,
        AUTHORITY["EPSG","8901"]],
        UNIT["degree",0.0174532925199433,
        AUTHORITY["EPSG","9122"]],
        AUTHORITY["EPSG","4277"]],
    PROJECTION["Transverse_Mercator"],
    PARAMETER["latitude_of_origin",49],
    PARAMETER["central_meridian",-2],
    PARAMETER["scale_factor",0.9996012717],
    PARAMETER["false_easting",400000],
    PARAMETER["false_northing",-100000],
    UNIT["metre",1,
        AUTHORITY["EPSG","9001"]],
    AXIS["Easting",EAST],
    AXIS["Northing",NORTH],
    AUTHORITY["EPSG","27700"]]

and should be added to the gdal-dat folder ( see below)

The program gdalwarp.exe come from http://www.gisinternals.com/release.php

It is downloaded as a zip file. Unzip it then open a powershell window, in the window set the following environment variables:

 $env:GDAL_DATA= "U:\Users\Alex\Documents\GDAL\bin\gdal-data"
 $env:Path += ";U:\Users\Alex\Documents\GDAL\bin\gdal\apps"
 $env:Path += ";U:\Users\Alex\Documents\GDAL\bin"

For convenience put these in U:\Users\Alex\Documents\WindowsPowerShell\\Microsoft.PowerShell_profile.ps1

and execute

 Set-ExecutionPolicy -Scope CurrentUser Unrestricted in powershell

Then in file explorer, navigate to directory containing aerial photos, do File→Open Windows Powershell, up arrow to retrieve old command and execute.